## Slide 1: Statistics Behind Error Analysis TIPL 4201 TI Precision Labs – ADCs
Created by Art Kay
Presented by Peggy Liska
Notes: Hello, and welcome to the TI Precision Lab discussing the statistics behind error analysis. Specifically, in this section we will learn the statistical implications of the typical and maximum data sheet specifications. Furthermore, we consider the difference between a worst case analysis and a statistical analysis looking at typical values.

## Slide 2: Find the worst case offset
Device | PARAMETER |  | MIN | TYP | MAX | UNITS
LMP8481 | VOS | Offset Error | -265 | ±80 | +265 | µV
OPA320 | VOS | Offset Error | -150 | ±40 | +150 | µV
ADS8860 | EO | Offset Error | -4 | ±1 | +4 | mV
Worst case offset at ADS Input
Worst case offset at ADS Input
This result may be statistically unrealistic
Notes: Let’s start with a basic error analysis to better understand the concept of calculating total offset error in a system. This slide shows the example circuit that we will use for this error analysis. It is a high-side current shunt monitor that will monitor currents from 50mA to 20A. Let’s find the offset error seen by the data converter considering all of the elements in the signal chain. The current shunt amplifier, U1, has a gain of 20, so the output offset is increased by 20. The buffer, U2, has a gain of 1, so the output offset from U1 directly adds to the offset of U2 and the ADC, U3. A common approach is to take the maximum limit for each of the three devices and add them directly to find the worst case offset. However, this calculation assumes that all three devices have a worst case offset at the same time. What is the statistical likelihood that all these worst cases line up at the same time? We will take a look at this in the next few slides.

## Slide 3: Statistics Behind Typical and Maximum
PARAMETER ADS8860 |  | MIN | TYP | MAX | UNITS
EO | Offset Error | -4 | ±1 | +4 | mV
EG | Gain Error | -0.01 | ±0.005 | +0.01 | %FSR
Notes: This slide shows the statistical background behind the typical and maximum specifications in a data sheet. For a zero-centered specification the typical value is the absolute value of one standard deviation plus the mean of the distribution. Often, the mean value is near zero. So, for the purposes of this discussion, we will assume that the mean is zero. In this example, the typical offset is ±1mV which corresponds to ±1 standard deviation. The maximum offset is a tested parameter, so any device that exceeds the maximum limit is discarded and will not be shipped to customers. Thus, the distribution is actually a truncated Gaussian distribution as there is no population above the maximum or below the minimum. The maximum limit is set on the tail of the distribution to minimize yield loss during manufacturing. Typically the maximum is set above 3 standard deviations. In this example you can see that the maximum was set to 4 standard deviations. Note that 68.27% of the population is inside the typical limits.

## Slide 4: Probability that we are near worst case
PARAMETER ADS8860 |  | MIN | TYP | MAX | UNITS
EO | Offset Error | -4 | ±1 | +4 | mV
EG | Gain Error | -0.01 | ±0.005 | +0.01 | %FSR
Notes: From a statistical perspective, how likely is it that we find a device is at the maximum limit? For this example, what is the probability that we get a device at exactly 4mV? Since probability is equal to the area under the curve, and the area under a single point is zero, technically the probably is zero. This isn’t very helpful, so let’s consider the probability that we are near the maximum limit. In this example, the probability that we are between 2mV and 4mV is 2.272%. This makes sense when you look at the measured histogram as you really can’t see any bins in this region. We will use this statistical information in the next slide to find the compounded probability that all three offsets from our example circuit are near the worst case value.

## Slide 5: Compounding probabilities “near” worst case
The probability that all three offsets are near worst case
The probability that all three offsets are near worst case
Notes: Here we show the Gaussian distribution for all three components based on the data sheet specifications. What is the probability that all three devices are near the worst case? You can see that for each device the probability of being near worst case is about 2%. Since the three distributions are random and uncorrelated, the compound probability that all three events occur simultaneously is the product of the three probabilities. Stepping through the math, you can see the probability that all the devices are near worst case is 0.0011%. You can imagine that as the number of components in the system increases, the probability that all are at the worst case value is very small. So, directly adding the worst case offset for each device isn’t the best approach for understanding a system’s total error. In the next slide we will look at an approach that gives a better statistical understanding of the errors.

## Slide 6: A more practical approach: use the typical limit
Typical offset at ADC Input
Typical offset at ADC Input
Notes: This slide shows the distributions for all three devices in the signal chain. Rather than adding the maximum values we will add the three distributions. The standard deviation of uncorrelated Gaussian distributions can be combined as the square root sum of the squares. In this example all the distributions are referred to the input of the data converter so the offset from U1 is multiplied by the gain of 20 we noted earlier. The standard deviation for the total combined offset distribution is ±1.887mV. Let’s take a closer look at the combined distribution.

## Slide 7: A more practical approach: use typical
Typical offset at ADC Input
Typical offset at ADC Input
Number of Standard deviations | Probability Inside limit | Probability Outside limit
±1∙σ | 68.27% | 31.73%
±2∙σ | 95.45% | 4.55%
±3∙σ | 99.73% | 0.27%
±4∙σ | 99.9937% | 0.0063%
±5∙σ | 99.99994% | 5.73∙10-5 %
±6∙σ | ≈100% | 1.97∙10-7 %
Set end system specifications based on risk tolerance
Notes: The final system distribution has a standard deviation of ±1.887mV. This is analogous to a typical of ±1.887mV for the system. But what is the maximum offset error for our system? The maximum can be set according to the risk tolerance in your system specification. The table shows what percentage of a population will be inside a limit set according to the number of standard deviations. For example, if the system specification maximum is set to ±3 standard deviations, then 99.73% of the population will be inside that limit and 0.37% of the population will fall outside of the limit. Depending on the requirement, a more conservative limit can be set. It is important to realize that most specifications like offset have other factors that can impact the total error. Be careful not to adjust the statistical limits beyond the worst case limit we started with. Remember, the actual distribution of the device is a truncated Gaussian distribution so the combined distribution will also be truncated at the worst case we calculated earlier.

## Slide 8: Thanks for your time! Please try the quiz.
Notes: That concludes this video – thank you for watching! Please try the quiz to check your understanding of this video’s content.