## Slide 1: Using SPICE Monte Carlo Tool for Statistical Error Analysis TIPL 4203 TI Precision Labs – ADCs
Created by Art Kay
Presented by Peggy Liska
Notes: Hello, and welcome to the TI Precision Lab covering statistical error analysis for data converters. Overall, this video will cover how a SPICE analysis option called Monte Carlo analysis can be used to determine a statistically valid estimate of gain error. The video will cover a step-by-step approach for running a Monte Carlo analysis on TINA spice, as well as explain how to interpret the results.

## Slide 2: Discrete resistor tolerance sets gain error
Notes: Let’s start by looking at the circuit covered in the TI Precision Labs video titled “Understanding and calibrating the offset and gain for ADC systems”. In this example, the gain error of the current shunt amplifier was specified in the device data sheet because its gain is set by internal resistors. In many cases, however, the gain is set by external discreet resistors. This example circuit shows a discreet implementation of a differential in differential out amplifier. The differential gain for this circuit is given by 2*(Rf / Rg), which is 0.04 in this case. So for a ±100V input signal the differential voltage delivered to the ADC is ±4V. The gain accuracy for this circuit depends on the tolerance Rf and Rg throughout this circuit. Often engineers will do a worst case analysis based on the resistor tolerance but as we mentioned before this can yield results that are statistically unlikely. The industrial version of TINA spice and many other spice simulators provide an analysis tool called Monte Carlo analysis that can be very useful for doing a statistical error analysis. This presentation will explain how to use the TINA SPICE Monte Carlo analysis tool.

## Slide 3: DC Transfer Function
Select “Vin” for the input and enter the range from “Start value” to “End value”
Notes: Before doing the Monte Carlo analysis, let’s look at the DC transfer function for this circuit. In TINA, use the “DC Analysis>DC Transfer Characteristics” option. In the “DC Transfer Characteristics” window, select “Vin” as the input. Enter the voltage range of -100V to +100V for the “Start value” and “End Value”. Press ok and you will get the graph shown at the right. This graph shows that for an input of -100V the differential output is positive 4V, and for an input of +100V the differential output is negative 4V. Doing a DC transfer function is a good way of confirming the nominal transfer function, but it doesn't consider resistor tolerance. This is where Monte Carlo analysis can help.

## Slide 4: Set tolerance on resistors and capacitors
Set to 1% or 0.1% per resistor spec
Gaussian Distribution
Click here to set the tolerance.
Notes: Before running the Monte Carlo analysis you will need to set the tolerance for each resistor and capacitor in the circuit. Just double click on the resistor and a window listing the parameters will pop up. Press the button next to the resistance and a window to set the “Tolerance Parameters” will pop up. In this window set the tolerance according to your design and use Gaussian for the distribution type. In this example we are using 1% resistors.

## Slide 5: Monte Carlo Analysis
99.73% sets the component tolerance to ±3 Standard deviations
More cases will give you a better statistical distribution. The max is 1000.
Note the default of 68.26% will not give realistic results for resistor and capacitor tolerance.
Select “Monte Carlo”
Notes: To turn on Monte Carlo Analysis select “Mode” under the analysis menu option. In the “Analysis Mode Selection” window, select “Monte Carlo”. For “Percentage of population” enter 99.73%. This sets the component tolerance to ±3 standard deviations for the Monte Carlo analysis. Thus in this example, ±3 standard deviations occurs at ±1%. What we are really doing here is forcing the majority of the Gaussian population to be inside the tolerance limits. Note that the default of 68.26% corresponds to one standard deviation and this is not practical for resistor and capacitor tolerances. After entering the “Percentage of population” enter the “number of cases” that will be run in the simulation. In this example we run the maximum of 1000 cases. This will cause the simulation to re-run 1000 times using random resistor values according to the Gaussian distribution. In general, you should set this number as high as possible to get a good statistical result. The only disadvantage to setting this to the maximum limit of 1000 is that it will increase simulation time.

## Slide 6: Monte Carlo for DC Transfer Characteristic
2. Press CTRL+Alt to select all
3. Select Process>Statistics
1. Run a dc transfer characteristic
Notes: Now that the Monte Carlo function is turned on, any analysis will run as a Monte Carlo analysis. In this example a DC Transfer characteristic run, so the DC transfer function is simulated 1000 times using random Gaussian resistor values for each simulation. Even though the results looks like a single curve, it actually contains 1000 closely spaced curves. Now we want to use these curves to get a statistically valid gain error. To do this we first need to select all the curves by pressing “CTRL+Alt”. Next under the “Processes” menu we should select “Statistics”.

## Slide 7: The cut option
Number of bins in histogram. 10 is usually sufficient
We generate the distribution from the vertical section at x=100
Zoom in
Use Cut option
Enter the X-axis value where the cut set is taken
Notes: Under “Statistics” we want to select the “CUT” option. Cut will select the distribution on the Y-axis for a particular value on the X-axis. In this case we want to look at the gain error at the ends of the transfer function, or where Vin = 100V. It is easer to understand the vertical cut set when looking at a zoomed in version of the transfer characteristic. In this graph you can see that there are many closely spaced curves that correspond to the different random resistor values. The X-axis value for the cut set, which is 100V in this example, is entered in the adjacent box. Finally, select the number of bars that will be displayed in the histogram. In general 10 is sufficient.

## Slide 8: Generate the statistical data and histogram
Press Calculate to get statistics, and draw to show histogram
Use to calculate gain error.
Press draw to get a graph of the histogram
 | For 68.26% of the population
 | For 99.73% of the population
 | For 68.26% of the population
 | For 99.73% of the population
Notes: Next press “calculate” on the statistics window. This will cause the mean and standard deviation of the cut set to be displayed. This information can now be used to calculate the gain error in percentage for our circuit. For a typical gain error corresponding to 1 standard deviation take the standard deviation and divide by the mean value and multiply by 100 to get percentage. A worst case estimate can be set using the statistical factors introduced earlier. For example, multiplying the typical gain error by three sets a maximum limit that will include 99.73% of the population.

## Slide 9: Thanks for your time! Please try the quiz.
Notes: That concludes this video – thank you for watching! Please try the quiz to check your understanding of this video’s content.