## Slide 1: 6a: Connect the hardware
Notes: For this experiment we will be using channel 3 on the precision labs hardware. First, set the jumpers as shown here. Connect the PSI to the PLABS board using the SMA cable, and connect the PHI to the PLABS channel 3 connector. Finally, connect the USB cables to the computer. Throughout this experiment we will test different amplifiers. Always be careful to install this amplifier right side up with the label at the bottom of the coupon card. For now you can leave the amplifier socket empty. Pause and connect the hardware.

## Slide 2: Start & Setup the Plabs-Power Scaling EVM Software
1. Select “Plabs-Power Scaling” from “start>All Programs”
2. The green hardware connected and teal PSI controls indicate that communication is established.
Notes: Now start the “Plabs-Power Scaling” software. If the hardware is connected correctly you should see the green “hardware connected” indicator, and the PSI controls should be colored teal. Pause and start your software.

## Slide 3: Calibrate system offsets
1. Set Jumpers as Shown. Remove coupon card from socket. Sampling rate will be adjusted automatically.
2. Press “continue” after the hardware is configured.
Notes: Before making any power measurements we need to calibrate the system. This calibration will eliminate the offset errors from the INA and ADC, so that we can get the best accuracy. To do this press the “calibrate” button. Once you do this you will see a window pop up that shows how the jumpers need to be positioned for this test. In this case the input is set to “AC_IN”, and the jumpers are in the “CAL” position. Also, make sure that no amplifier is in the socket during this test. Press “continue” after the hardware is configured. Pause and calibrate the system.

## Slide 4: Measure OPA320 at different sampling rates
Start by measuring system power at 1Msps and 500ksps. At these sampling rates we will use the OPA320.
Change the jumpers as shown. Install the OPA320_Good_filter2 device.
Press continue to measure power at the specified sampling rate.
Notes: Now we are ready to start measuring power. First we will measure the OPA320 and ADC at high sampling rates. Press the 1Msps button to begin. This will bring up a window that shows how to set the jumpers and indicates that you need to install the “OPA320 Good Filter 2” coupon board. Make these changes in the hardware and press continue. Follow the same procedure for the 500ksps sampling rate. Pause and make these measurements.

## Slide 5: Compare final test results to calculated values
Select the “Power” cells in the measured table. Right click and “Export Data to Excel”.
Notes: To compare the measured results to the calculate results you should export the data to Excel. To do this highlight the power cells in the GUI table and right click. Select “Export Data to Excel”. This will cause an Excel spreadsheet to pop-up with the measured data. Now we can paste this into our table for comparison. Pause and export the data to Excel.

## Slide 6: Measured vs Expected Results
Your results should show the same trend as the expected result but the specific values will differ.
 |  | Calculated |  |  |  | Example Measurements |  |  | 
Amp | Sampling Rate | PDVDD (µW) Max | PAVDD (µW) Max | PQ_Amp (µW) Max | PTOTAL (µW) Max | PDVDD (µW) | PAVDD (µW) | PQ_Amp (µW) | PTOTAL (µW)
OPA320 | 1M | 1306.80 | 690.00 | 7875.00 | 9871.80 | 639.57 | 645.08 | 6461.89 | 7746.53
OPA320 | 500k | 653.40 | 345.00 | 7875.00 | 8873.40 | 282.36 | 321.95 | 6468.08 | 7072.39
TLV313 | 100k | 130.68 | 69.00 | 405.00 | 604.68 | 57.75 | 64.10 | 177.09 | 298.94
TLV313 | 10k | 13.07 | 6.90 | 405.00 | 424.97 | 6.67 | 6.50 | 176.94 | 190.11
LPV811 | 1k | 1.31 | 0.69 | 2.43 | 4.43 | 0.38 | 0.64 | 1.81 | 2.83
LPV811 | 200 | 0.26 | 0.14 | 2.43 | 2.83 | 0.06 | 0.13 | 1.81 | 2.00
Notes: This table compares the calculated result to the measured results. Here the example measurements are pasted in. It is important to note that the calculated results use data sheet maximum values, so you should expect that the calculated results are larger than the measurements. A quick review of the data shows that the measurements are smaller than the calculated maximum as expected. Nevertheless, you can see that the calculated and simulated results are in the same range and the measured trends match the calculated trends. Also, notice that the amplifier current is only dependent on the amplifier type and not on the sampling rate. Finally, notice the profound impact that changing the sampling rate has on total power. At full sampling rate the total power is 7746uW, and at 200sps the power is 2uW.

## Slide 7: 6b: Measured vs Expected Results
 |  | Calculated |  |  |  | Your Measurements |  |  | 
Amp | Sampling Rate | PDVDD (µW) Max | PAVDD (µW) Max | PQ_Amp (µW) Max | PTOTAL (µW) Max | PDVDD (µW) | PAVDD (µW) | PQ_Amp (µW) | PTOTAL (µW)
OPA320 | 1M | 1306.80 | 690.00 | 7875.00 | 9871.80 |  |  |  | 
OPA320 | 500k | 653.40 | 345.00 | 7875.00 | 8873.40 |  |  |  | 
TLV313 | 100k | 130.68 | 69.00 | 405.00 | 604.68 |  |  |  | 
TLV313 | 10k | 13.07 | 6.90 | 405.00 | 424.97 |  |  |  | 
LPV811 | 1k | 1.31 | 0.69 | 2.43 | 4.43 |  |  |  | 
LPV811 | 200 | 0.26 | 0.14 | 2.43 | 2.83 |  |  |  | 
Notes: Now you can paste your measured results into the table. You should confirm that your results are in the same range as the hand calculations. Pause and paste your results into the table.