## Slide 2: Agenda
Architecture options
Sitara AM64x for motion control
Fast Serial Interface (FSI)
C2000 real-time microcontrollers for motor control
Get started

## Slide 3: Architecture

## Slide 4
Centralized and decentralized multi-axis servo control
Decentralized
Control loop processing distributed across system
Isolated communication between control boards
Simplified motion control board
Centralized
Control loop processing all in one location
Isolated actuation/feedback signals
Simplified power stage boards
Notes: This slide shows a two-chip solution, with the two system on chips (SoCs) separated by the isolation boundary. The benefit of this architecture is that the total time for the field-oriented control loop (or torque loop) to get inputs from the motor and return a current is small because the entire processing loop runs locally on the power stage board.
The partitioning shown here is a very common one. Many real-time controllers capable of closed-loop control of a servo motor (including interfacing with the phase currents and gate drivers of the power stage board) are not fully equipped to handle Ethernet-based industrial communication protocols. This leads to this two chip solution where one SOC provides communication and the other SOC provides motor control. A perfect example of this type of system is a C2000 device controlling the motor with a low-cost AM3359/AMIC110 device providing Industrial Ethernet.
One thing to note in this type of system is that the communication between the two SOCs must cross the reinforced isolation boundary. Isolation ICs are required to protect these signals and depending on the width of the bus this can become expensive. For this reason a fast, low pin count serial interface is ideal to keep cost down while still achieving the data movement requirements needed to close the outer processing loops. The Fast Serial Interface (FSI) from C2000 was created specifically for this purpose in this type of system partitioning. Up to 200Mbps speeds can be achieved with as few as 3 signals using FSI.

## Slide 5
Where and why to use decentralized control
Where?
Multi-axis robotics
Linear transport systems
CNC machines
Autonomous Guided Vehicles
Why?
More intelligence at the motor drive
No external control cabinet needed
Reduced system cabling costs
Improved control loop performance
Notes: This slide shows a two-chip solution, with the two system on chips (SoCs) separated by the isolation boundary. The benefit of this architecture is that the total time for the field-oriented control loop (or torque loop) to get inputs from the motor and return a current is small because the entire processing loop runs locally on the power stage board.
The partitioning shown here is a very common one. Many real-time controllers capable of closed-loop control of a servo motor (including interfacing with the phase currents and gate drivers of the power stage board) are not fully equipped to handle Ethernet-based industrial communication protocols. This leads to this two chip solution where one SOC provides communication and the other SOC provides motor control. A perfect example of this type of system is a C2000 device controlling the motor with a low-cost AM3359/AMIC110 device providing Industrial Ethernet.
One thing to note in this type of system is that the communication between the two SOCs must cross the reinforced isolation boundary. Isolation ICs are required to protect these signals and depending on the width of the bus this can become expensive. For this reason a fast, low pin count serial interface is ideal to keep cost down while still achieving the data movement requirements needed to close the outer processing loops. The Fast Serial Interface (FSI) from C2000 was created specifically for this purpose in this type of system partitioning. Up to 200Mbps speeds can be achieved with as few as 3 signals using FSI.

## Slide 6: Example AM64x + F28002/4x decentralized architecture
AM64x
F28002/4x LaunchPad(s) +
Power Stage Boosterpack
ARM
Cortex A53
ARM
Cortex A53
(Motion)
C28x
(Current/
FOC)
M
Encoder
C28x
(Current/
FOC)
M
Encoder
FSI
C28x
(Current/
FOC)
M
Encoder
FSI
FSI
ARM
Cortex R5F
(Position/
Speed)
ARM
Cortex R5F
(Position/
Speed)
ARM
Cortex R5F
(Position/
Speed)
ARM
Cortex R5F
(Position/
Speed)
Reinforced
Isolation
Boundary
Multi-protocol Industrial Ethernet
Integrated Motion Control
Centralized Multi-axis Position/Speed
Control
Fast, low-pin count communication
Distributed Current/FOC Control

## Slide 7: Demo
https://training.ti.com/decentralized-multi-axis-motor-control
Sitara™ AM64x processors: Outer control loops with CiA402 drive profile run on a Sitara™ AM64x processor using EtherCAT® communication from a PC
Adapter boards: Real-time, low pin-count, robust communication up to 200 Mbps over Fast Serial Interface (FSI) adapter boards
C2000™ real-time controllers: Inner current loops run on F2800x LaunchPad™ development kits
BoosterPack™ development kits: GaN three-phase inverter BoosterPack™ development kits

## Slide 8: Sitara AM64x Processors

## Slide 9: AM64x
Cores & Memory
  Dual Cortex-A53 up to 1GHz
  Quad Cortex-R5F up to 800MHz
  2MB on-chip SRAMECC on all critical memories
  16b LPDDR4/DDR4 controller with inline ECC
Industry 4.0 Services
  Dual-core Arm Cortex-A53 cores capable of running RT Linux enable high-level applications and networking
Multi-axis Control
  Up to 4x Arm Cortex-R5F cores running at 800MHz provide more than 5,000 DMIPs of processing for real-time control tasks
Fast Serial Interface
  FSI allows fast, serial communication across isolation boundaries with multiple C2000 devices
Multiprotocol Industrial Communications
  PRU-ICSS(Gb) subsystem integrates EtherCAT, PROFINET, EtherNet/IP capability into a single package

## Slide 10: Industry 4.0 services
PLC/Motion Controller
Servo drive
PLC/Motion
Controller
Servo drive
Saves space and cost
Faster possible refresh rates
Seamless compatibility between amplifier and PLC
Integrated Motion Control
Voltage analysis
Vibration analysis
Current analysis
Magnetic field analysis
Ultrasonic analysis
Thermal analysis
PdM
Predictive
Maintenance
Predict remaining useful life
Predict time to failure
Remote
Control
Check real-time status of machinery
Update control parameters remotely
Notes: Customers are looking to compete by offering cost savings to the machine builders through integration of PLC/Motion control and servo drive. There’s integration at both ends of this system: Motion controllers are integrating servo drives (or “amplifiers”), and the servo drives are integrating motion controllers. Integration of these functions saves cost, space, and headaches for machine builders who would otherwise need to ensure compatibility between PLCs and drives. On top of that, there are system level benefits like the potential for faster refresh rates since the PLC and drive can use high speed interfaces like PCIe or wide parallel buses to pass data back and forth (or they can even both be handled on the same SoC).

## Slide 11: Multi-axis, real-time control
Arm Cortex-R5F cores running at 800MHz provides greater than 5,000 DMIPs of processing power
  Allows for tighter control loops, more advanced algorithms, and more background processing
Tightly-coupled memory (TCM) for each core to allow deterministic, single-cycle access for instruction and data
  Guarantees real-time deadlines are met on each iteration of the loop
Up to 4x Arm Cortex-R5F cores provides software partitioning options
  Pipelined approach: each core handles a specific function for all axes and then passes the result to the next stage in the pipeline
  Distributed approach: each core handles all control code for one or more axes
Software Development Kit provided including Real-time operating system (RTOS) and control libraries
  Decrease getting started and overall development time
Notes: Customers are looking to compete by offering cost savings to the machine builders through integration of PLC/Motion control and servo drive. There’s integration at both ends of this system: Motion controllers are integrating servo drives (or “amplifiers”), and the servo drives are integrating motion controllers. Integration of these functions saves cost, space, and headaches for machine builders who would otherwise need to ensure compatibility between PLCs and drives. On top of that, there are system level benefits like the potential for faster refresh rates since the PLC and drive can use high speed interfaces like PCIe or wide parallel buses to pass data back and forth (or they can even both be handled on the same SoC).

## Slide 12: Multiprotocol industrial Ethernet
Sitara improves the overall development process and supply chain by:
  Enabling re-allocation of inventory from one protocol to another in minutes to meet sudden demand changes
  Narrowing down hardware procurement to a single vendor
  Drastically reducing inventory management complexity
  Providing a single hardware design to meet the needs of multiple markets
Profinet IRT/RT
SKU
EtherNet/IP
SKU
EtherCAT
SKU
Profinet IRT/RT module
EtherNet/IP module
EtherCAT module
Inventory
Communication module
Profinet IRT/RT ASIC
EtherNet/IP ASIC
EtherCAT
ASIC
Communication device
The typical multi-protocol design process has many disadvantages including:
  Complex inventory management and accurate forecasting needed for each individual protocol
  Multiple silicon suppliers required
  Separate hardware designs for each protocol
  Expensive total cost when using multiple ASICs
Traditional flow
Profinet IRT/RT
SKU
EtherNet/IP SKU
EtherCAT SKU
Multi-protocol board
Inventory
Communication module
Sitara™ processors
Communication device
Flow with Sitara
Notes: This is a visual of how complex a traditional multiprotocol supply chain would look
  A different ASIC for every protocol which can be expensive
  A separate hardware design since each ASIC has its own board requirements
  Different inventory materials as one board for every protocol must be stocked
This custom flow for every protocol adds pressure on forecasting demand accurately for each protocol

## Slide 13: FSI

## Slide 14: TI’s FSI vs. standard serial interfaces
Very Low Signal Count
Standard LVCMOS IO Buffer
Low Latency & up to ~200 Mbps BW
FSI
Standard SPI
SERDES/LVDS
RapidIO
PCIe
I2C
SD I/O
QuadSPI
Uniquely meets the three key criteria:
  Very low signal count
  Standard LVCMOS IO buffer
  High bandwidth
FSI includes:
  On-the-fly CRC calculation
  Hardware watchdog
Use Cases:
  High speed communications across air gap for power electronics isolation
  On board chip-to-chip topologies
  Alternative to parallel/EMIF interfaces
Available on select TI processors, microcontrollers, and library for FPGA

## Slide 15: Enabling new options for drive architectures
Fast Serial Interface (FSI) enables high speed (200 Mbps/3-wire or 100 Mbps/2-wire) chip-to-chip communications while leveraging the latest in TI’s galvanic isolation technology.
Benefits
Reduces need for isolation components
Enables real time loops to span air gap
Enables new drive architectures
  Smart sensing/Data concentrator
  Smart sensor/resolver/position sensor
  Host/Slave controller
  Loop controller – actuation/sensing
  Alternative to mixed signal ASIC/FPGA
Features
Fast transfer (100-200Mbit/sec @50MHz CLK)
Line break detect
  Ping frame: periodic frame for line break detect
  Frame watchdog on receiver
HW CRC- polynomial calculation and checker
Signal line skew compensation
Customizable tags and data
Flexible topologies: point-to-point, star, daisy-chain

## Slide 16: C2000 real-time microcontrollers

## Slide 17: Integrated innovation: www.ti.com/c2000drives Lowest latency, highest precision, minimum jitter
PWM Customization
PWM Protection
Industrial Communications
UART
CAN
USB
I2C
Ethernet
More …
Position Sensor Interface
Pulse Train Output / Input
Actuation
PWM
three-phase inverter
PM
motor
Position
sensor
SD
Filters
ADC
PWM
Trip
Fluxgate
sensors
DS isolated
ADCs
eQEP
ADC
DAC
Isolated
shunt current
buffer
Drive
Control
SOC
Isolated
gate drive
Sensing
Protection
Line
Interface
Processing
DAC
150 ps resolution
Deadband Gen
Autonomous ADC Trig
>60x8 Trip XBAR
Protection
50 ns to PWM trip
Up to 16-bit, 4 MSPS
Up to 12-bit, 12 MSPS
Digital Post Process
High Precision
Up to 8 Channels, with compare
Digital and Analog
Position Sensor Interface
EnDat, BISS, t-format,
HDSL, SSI
Resolver, SIN/COS
C28x™
Core(s)
CLA
Core(s)
Flash
RAM
ROM
RAM
RAM
ROM
0 ws
0 ws
0 ws
0 ws
Wide access
0ws
0ws
Deterministic pre-fetch
Zero wait-state linear code
High determinism
Fast interrupt response
Atomic ALU
Linear memory space
Zero wait-state RAM, ROM
Shared RAM between cores
EMIF
Memory
Sitara™
DZ Security
Trig Accelerator
Floating Point
Configurable Logic
Block
SPI
FSI
secondary
controller
< 500 ns calculation for FOC control loop
Functional Safety
SIL-2 Random Hardware Component Use in SIL-3 systems
TUV certifications and servo drive concept reports available

## Slide 18: Get started

## Slide 19: Getting started
FSI documentation
  See Device TRMs ex: TMS320F28002x Technical Reference Manual
  Using the Fast Serial Interface (FSI) With Multiple Devices in an Application
  Fast Serial Interface (FSI) Skew Compensation
Evaluation modules
  TMDSFSIADAPEVM
  LAUNCHXL-F280049C
  LAUNCHXL-F280025C
  BOOSTXL-3PHGANINV
  TMDS64GPEVM
Reference designs
  TIDM-02006 (C2000 F2838x outer loop controller – FSI – F28004x/2x nodes)
  AM64x Software Development Kit with FSI based Decentralized Servo example
  AM64x + C2000 decentralized servo demo

## Slide 20: Q&A

## Slide 21
SLYP744