## Slide 1: New TI smart analog and smart DAC for adding intelligence to analog without software at low cost
Uttama Sahu
Data Converters - DAC

## Slide 2: Abstract
Control w/o software
Smart DACs
Sensing and control w/o software
Smart AFEs
System designers often need simple software solutions to attain predictable system power up and tunable set points
TI’s innovative smart AFE and smart DAC portfolio provides simple intelligence to an analog system designer without the need for MCUs
TI’s smart analog products, have NVM and factory programmable state machines, internal ADCs, DACs, PWM generators, custom waveform generators
Analog and software engineers can reduce system costs, remove tiny MCUs, and expedite design cycles

## Slide 3: Agenda
Current day challenges in system design
What are smart DACs and smart analog
Example smart DACs
Smart DAC applications
Example smart analog
Smart analog applications
Summary
3

## Slide 4: Current-day challenges in system design
Design
Pros
Cons
Discrete circuit
MCU-based circuit
Low Cost
Optimized design
Difficult to design
Difficult to scale / reuse
Needs strong analog design expertise
Many components need bigger area
Manages complexity
Easy to reuse
Software dependence for simple logic and configuration
Higher R&D time and cost
Software maintenance and certification overhead

## Slide 5: Why smart DACs and smart AFEs
MCU
Analog design is fun. Adding programmability is not …
SW for differentiation
Smart DACs/AFEs
Add programmability and logic
without SW
Discrete components
DACs
Now you have smart DACs and smart AFEs
Programmability and precision
Simplicity
Programmability
No MCU
No software

## Slide 6
Hi-Z
GPI Trigger
NVM
Comparator
DAC
(Ultra Low-Power)
What is a smart DAC?
PWM
- control w/o software
Alarm
Programmable current limit
TPL1401
Latching comparator
DAC53701
PWM output
DAC53701
Change output with GPI trigger
DAC53701
Alarm when MCU fails
DAC53701
Hassle-free voltage margining
DAC53204

## Slide 7
NVM
PWM
DAC
ADC
State Machine
GPI Trigger
What is smart AFE?
Analog to PWM
Logarithmic fade-in fade-out
Cascaded animation
Closed-loop control
- sensing and control (w/o software)
DAC53902-Q1
AFE539B4-Q1
DAC539x4-Q1
AFE53902-Q1

## Slide 8: An example smart DAC
Internal reference with 1% accuracy
User programmable Nonvolatile memory
Buffered wiper for improved load regulation
Hi-Z or programmable start-up using NVM
Lock bit to protect accidental writes to register or NVM
I2C interface
Wide temperature range: -40°C to +125°C
Small package WQFN-8 (2x2)
TPL1401

## Slide 9: Generating a DC set-point
Resistor divider
Shunt regulator
LASER trimming
Load regulation
Force-sense output enables current output and comparator
Provides programmability
Retains configuration
Provides load regulation
TPL1401 differentiation
Example application
Integrated reference
Simple circuit
No programmability
No load regulation
External reference
Limited programmability
No load regulation
External reference
No programmability
No load regulation
Large area
Limited programmability

## Slide 10: Adjustable current limit
LED driver, DC-DC converter
Power amplifier
E-fuse, High-side switch
Standalone battery charger
Standard digipot
TPL1401 differentiation
Integrated reference provides 1% accuracy
EEPROM with > 40 years usable life at 125 oC
Digipots are commonly available in 20% tolerance
Higher accuracy digipots are expensive

## Slide 11: LASER diode analog power control (APC)
Resistor divider
Standard digipot
TPL1401 differentiation
Simple way to set an accurate bias point for the LASER
Program at factory and eliminate run-time programming
The high-speed modulation DAC need not take the load of controlling the biasing dynamically
External reference
Digital programmability
Larger area
External reference
Limited programming steps
Larger area

## Slide 12: An example smart DAC
GPIO configurable as power-down, PWM input, function trigger, or fade-in fade-out trigger
User programmable Nonvolatile memory
PWM output using free-running triangular waveform and FB pin
I2C interface
Wide temperature range: -40°C to +125°C
Small package WQFN-8 (2x2)
DAC53701-Q1

## Slide 13: Appliance light fade-in fade-out
GPI based fade-in fade-out
Programmable slew rates from milliseconds to 5 seconds
Programmable min and max output levels
GPI can be directly connected to mechanical switch without MCU/software
DAC can drive either an LED driver or directly drive LEDs using a MOSFET

## Slide 14: Voltage margining and scaling
Hi-Z power-down by default
Digital slew rate control for glitch-free voltage scaling
GPI to take the output to Hi-Z or other safe level when software crashes or during brown-out
I2C and PMBus compatible interface
NVM for predictable power-up

## Slide 15: Programmable comparator
Programmable hysteresis and latching functions independent of MCU
10-bit comparator threshold
10-bit hysteresis programmed using margin-high and margin-low registers
Latching comparator function
EEPROM retention > 40 years at 125 oC operating temperature, suitable for industrial applications
Programmable hysteresis
(GPI mapped to margin-high/low)
Latching comparator
(GPI mapped to power-up/down)
Programmable
comparator
Programmable
hysteresis
Latching
comparator
Comparator threshold is programmed in DAC-DATA register
GPI is unmapped
GPI mapped to margin-high (GPI HIGH) and margin-low (GPI LOW)
DAC-DATA is same as either margin-high or margin-low
DAC output is pulled up by a resistor to VDD
GPI mapped to power-up (GPI HIGH) and power-down to 10K (GPI LOW)
DAC-DATA is the comparator threshold
DAC output is pulled up by a resistor to VDD

## Slide 16: Medical alarm
In-built alarm timings as per IEC60601-1-8 standard – register based configuration
One DAC is used for generating the trapezoid with timing and gain control
Another DAC is used to generate the alarm tone
Directly trigger high-priority alarm using GPI
Low-power consumption enables smaller battery back-up for power failure alarm

## Slide 17: Temperature to PWM converter
NTC resistance to PWM conversion
PWM interfaces needs only single-wire – suitable for isolation barriers
PWM duty cycle proportional to NTC resistance
Factory programming of PWM frequency through triangular / sawtooth waveform in NVM
No run-time software required

## Slide 18: STOP tail lighting
PWM (~200 Hz) with constant duty cycle
GPI based dimming when trunk is opened or closed
Software programmability of PWM frequency through triangular / sawtooth waveform
Better intensity matching between the trunk and fender lights (< 1% duty cycle accuracy) as compared to 555 timers
1
1
1
0
1
0
0
0
30%
40%
60%
70%
Trunk
Fender

## Slide 19: LED and temperature
LED reliability
LED reliability is significantly determined by the operating temperature
LEDs in DRLs are heated by both self-heating and sunlight
Daytime running light (DRL)
Source: https://www.linkedin.com/pulse/high-temperature-enemy-led-performance-what-you-need-know-floroiu/
Notes: Sources:
https://www.ledrise.eu/blog/led_high_temperature_performance_explained-lr/
https://www.ledrise.eu/blog/led_high_temperature_performance_explained-lr/
https://www.led-professional.com/resources-1/articles/reliability-oriented-design-of-led-based-light-sources-by-the-university-of-padova-and-lightcube-srl

## Slide 20: Single-slope thermal foldback
Processor-less single-slope thermal foldback for DRL
Software programmable knee point and slope
PWM with duty cycle following foldback curve
Software programmability of PWM frequency through triangular / sawtooth waveform
Optional voltage output with RC filter

## Slide 21: An example Smart analog frond end (AFE)
User programmable Nonvolatile Memory (NVM/EEPROM)
I2C and SPI mode auto-detection
GPIO interface
PWM output
Hi-Z output during power-off condition
10-bit ADC mode for all channels
Control logic that supports look-up table and closed-loop control
Wide Temperature range: -40°C to +125°C
Small package WQFN-16 (3x3)
AFE539x4-Q1

## Slide 22: TEC control
Predictable power-up when the software is not ready
Integrated DAC and ADC for closed-loop control
Simple closed-loop control w/o run-time software
Direct NTC interface

## Slide 23: TPL1401 application summary
Losing yield at factory? Does the voltage need tuning at factory or at the field?
Does the PCB need HW change for every new revision?
Are you struggling to find the right way to generate a DC set-point?
LASER diode
Voltage divider, Adjustable shunt regulator
LEDs
Adjustable current limit
Microphone tuning
Adjustable reference

## Slide 24: DAC53701 application summary
Are you using an MCU just to create an adjustable PWM? Are you stuck with a 555 timer?
Are you avoiding simple fade-in fade-out effects in lighting because of cost?
Do you often notice fault management designs to be tricky?
Voltage margining and scaling
Fade-in fade-out
PWM output
Medical alarm
Temperature/Resistance to PWM
Programmable comparator

## Slide 25: DAC53204 application summary
Does your system require accurate bias points?
Does your voltage margining circuit require a DAC that has Hi-Z output even during power-off?
Do you often notice fault management designs to be tricky?
Programmable Comparator
Voltage margining and scaling
LASER amplifier control
Amplifier and VCO biasing
MEMS LIDAR scanning
Ultra-low power LED biasing

## Slide 26: AFE539x4 application summary
Are you using an MCU to create simple control loops?
Does your system have shortage of GPIOs or have the need for long-distance control over GPIOs?
Are you burdened by software to create LED animations?
Logarithmic fade-in fade-out
TEC control, PI control
PWM IO expander
Multi-slope thermal foldback
Dynamic headroom control
LED animation

## Slide 27
SLRP001