## Slide 2: Acknowledgement
Jeff Mueller
Richard Herring
Derek Payne
Mateo Begue
Ritesh Oza
Wei Zhang
Don Dapkus

## Slide 3: What will I get out of this session?
Purpose:
  Gate driver Fundamentals
  Common issues, solutions and design practices on:
    Bias/bootstrap supply
    Open functional pins or connect with Hi-Z
    Parasitics
    dv/dt noise
    Variance
Part numbers mentioned:
  UCC27282
  UCC27710
  UCC27284-Q1
  UCC27201
  UCC27524
Relevant applications:
  Motor drive
  Switch mode power supplies
  Solar inverters
Notes: Hello and Welcome, everyone. My name is Mamadou Diallo. I'm an applications engineer in the high power drivers group.
This presentation will discuss pitfalls related to gate drive circuits in automotive & industrial applications specifically driver biasing, bootstrap supply, and its component selection necessary to generate high side bias. I will also discuss the effect of open functional pins and the impact of dv/dt noise in gate drive circuits.
I will Then identify parasitics and, finally, show issues related to poor layout and how to correct them.
The part numbers mentioned in this presentation will include the 620V half-bridge driver with interlock, UCC27710; the 120V half-bridge gate drivers with integrated boot diode, UCC27201, UCC27282, UCC27284-Q1 and the dual low-side gate driver UCC27524.
The topologies I will discuss today are relevant to motor drive, switch mode power supply, as well as solar inverters applications. This presentation is meant to be interactive, so for each issue, I will first show some wave forms and schematics, then I will start a polling to give you a chance to identify the problem and possible root causes before finally sharing the answer.

## Slide 4: Where are gate drivers used?
Electric vehicles
class D audio
Renewables
Solid state lighting
(SSL)
Adaptors and
chargers
Server/telecom/UPS
Gate driver
applications
Motor drive (VFD)
Li-ion battery portables
Notes: Where do you find gate drivers?
Applications for gate drivers are very wide and I name a few here, Like Battery Management Systems for portable devices and its adaptors.
Server/Telecom/UPS, EV charger/motor drive/ as well as Class D audio.
Appliances in the kitchen, renewables and solid state lighting.
Generally speaking, gate drivers have been used everywhere for efficient power conversion.

## Slide 5: Fundamental Component in Power Electronics
Power Switches control flow of current in power electronic circuits by operating in 2 states (ON/OFF)
GATE (G) terminal controls ON/OFF status of switch
Input (VIN, IIN, PIN)
Switch-Mode
Power Converter
Output (VOUT IOUT, POUT)
AC-DC (or) DC-DC (or) DC-AC
Si  GaN and SiC
CGS
CGD
G
D
S
(Gate-to-Source Voltage) VGS
ON
ON
OFF
OFF
Threshold
To turn ON: Apply a positive voltage, VGS > Threshold level
To turn OFF: VGS < Threshold level
MOSFET
Notes: Modern Power Electronics are dominated by Switch Mode Power conversion;
Commonly used devices for power switching are MOSFET and IGBT and these have two states ON/OFF controlled by gate terminal.
GATE terminal controls the ON/OFF state of transistor
VGS = Voltage Between Gate & Source
To turn ON: Apply a positive VGS voltage greater than the specified Threshold level
To turn OFF: VGS must be lower than the threshold level
The GATE is a capacitive input, high-impedance terminal
There are 2 parasitic capacitors inside the MOSFET internal structure (CGS, CGD)

## Slide 6: #1 What is wrong with VCC?
Causes
  Low capacitance on VCC
  Capacitor placement/layout
  Biased capacitance (C vs. V)
  Temperature (C vs. temp)
  Capacitance aging
Consequences
  Driver malfunction
  UVLO tripping
  EMI noise
VCC
HO
LO
Very high ripple
Bias supply
Notes: All right, let's get started. For our first issue, closely look at the wave form and schematic provided.
This is a half-bridge configuration where a PWM signal is controlling the driver's input.
The bootstrap circuitry-- composed of Cbias on VCC pin, the boot cap or HB_HS capacitor, and the boot diode. This bootstrap network generates bias for the Q1 FET during the high side on time. This high side FET Q1 is referenced by design to the switch node HS. The driver's low side output LO buffers the PWM signal to the Q2 FET reference to ground.
What is could be wrong with the VCC supply? What could be causing the issue?
I will go ahead and open a poll to give you a chance to identify the issue and possible root cause.
Notice on the schematic, Cbias equals Cboot equal 1uF each. This situation may cause very high ripple on the VCC supply, leading to driver malfunction, as shown on the waveform where HO and LO are simultaneously switching, potentially causing shoot-through.
As it is, the bias cap is not correctly sized to allow for capacitance shift occurring from DC bias and temperature variations. This can lead to UVLO tripping if the ripple on the VCC reaches the UVLO threshold and disable the gate driver. Another result from this issue is the circuit being susceptible to EMI noise.

## Slide 7: #1 VCC bias capacitor considerations
Increase VCC bias capacitor
Rule of Thumb:
Place the VCC bias capacitor very close to the VCC pin of the driver
Sizing VCC bypass capacitor
  ΔVHB = VCC - VDF - VHBL
  CBOOT = QTotal / ΔVHB
  CBias >> CBoot
  High freq. filter capacitor
Notes: To address this issue, we first need to size the bias capacitor correctly. The charge to replenish the bootstrap capacitor must come from the VCC bypass capacitor.
As a general rule of thumb, C bias should be sized to be at least 10 times larger than the boot cap so that it is not completely drained during the charging time of the boot cap. This allows the boot cap to be properly replenished during the charging sequence. This 10x ratio result in 10% maximum ripple on the VCC capacitor in worst case conditions.
An alternate method to determine C bias is also included in the bottom right corner. It consists of determining the maximum desired ripple on the HB supply delta HB knowing the supply voltage of the gate driver IC, the boot diode forward voltage drop found in the diode datasheet AND the HB pin UVLO falling threshold found in the gate driver datasheet. From there, the min allowed bootstrap capacitor is determined through the ratio of the total gate charge and delta HB. The maximum value for this cap will vary by application.

## Slide 8: What is wrong with HO waveform?
Causes:
  Low capacitance
  Low Rgs
  Low Fsw
  Large D
Consequences:
  Hot MOSFET
  Output ripple
HO drooping / Bootstrap leakage
Bias supply
Notes: This next issue shows another waveform of a half-bridge configuration. Ch-1 in yellow is the high side input. Ch-2 shows the switch node in red, CH-3 in blue is the low side output, and CH-4 captures the high side output HO. What could be wrong with the HO waveform? Please take a moment to think of an answer.
Did you notice the leakage occurring on the high side gate?
This HO leakage can be caused by a combination of many factors, including low boot cap values not capable of storing the required energy to drive the high side FET.
Another common reason for this may be related to low gate-to-source resistance on the high side. A 3rd probable cause for this might be switching at low frequencies. All of these causes could lead to heating across the junction terminals of the MOSFET as well as ripple on the output.

## Slide 9: #2 bootstrap capacitor considerations
Increase Cboot
Increase Rgs
Place the boot capacitor very close to the HB-HS pins of the driver
Sizing bootstrap capacitor
CBoot = QTotal / ΔVHB
QTotal = QG + (IHBS x DMax/FSW) + (IHB/Fsw)
Notes: Solutions to this problem include increasing the bootstrap cap in order to provide the required bias to the high side gate. Increasing the gate to source resistor also helps resolve this issue.
After implementing the changes, it is also critical to maintain the HB_HS capacitor very close to the driver's HB_HS pins.
Shown on the bottom right corner is how to correctly size the HB_HS capacitor knowing the Power transistors total gate charge and the maximum allowed voltage ripple on HB_HS.
Similar to the first section, depending on application, one may approximate the HB_HS capacitor to be 10 times that of the gate to source capacitance.

## Slide 10
Design guidelines
Reduce RBoot
Minimum top switch ON time
HS waveform – inconsistent HS signal
Very short LO duty cycle – partially charged CBoot
#2 What is wrong with switch node waveform?
Bias supply
Notes: For the next common issue, we still have the same topology from the previous example.
Ch-1, the yellow waveform captures the HB to VSS voltage; ch-2, the blue waveform shows the HO to VSS signal; and ch-3 captures the HS switch node in pink. Do you see anything wrong with the waveform?
Did you identify the inconsistent HS waveform? Notice that, during some pulses, the HS signal is switching close to GND while other pulses are limited to 15V-18V? This is typically related to the HB_HS capacitor not fully charging during the low side FET on time.
Keep in mind that the bootstrap capacitor must be allowed to fully replenish every time that the low side FET is on. As it is, the low side transistor on time is too short due to long duty cycles on high side and preventing HS to switch close to GND. The minimum bottom FET on-time is determined such that it is greater than t = CHB_HS * R. R being the series bootstrap resistor.
One possible solution to this issue is to reduce the bootstrap resistor in order to allow peak current from the bias supply to quickly charge the HB_HS capacitor.
The time constant RC may be tuned to achieve the desired startup time.
Another solution to this problem is to ensure sufficient minimum on time for the low side switch, which will allow the HS pin to switch close to GND for the HB_HS cap to fully replenish.

## Slide 11
HS neg. ringing  overcharging the boot cap
Fast HS slew rate  noise and oscillation on HB
Noise and overcharging of HB
Design guidelines
Increase boot resistor
Increase boot capacitor
#3 Is this waveform normal?
Bias supply
Notes: On this next common issue, it is still a half-bridge topology. On the right, ch-1 in yellow captures the HB_VSS signal, and ch-3 in pink captures the low side output LO. Can you spot the problem here based on the waveforms shown?
Did you notice the long duty cycle operation on the LO channel? If so, that is good critical point. That is causing overcharging of the bootstrap capacitor through the red path highlighted.
Notice that this is the opposite of the previous situation where the low-side FET had too little duty cycle.
In this case, the on time of the low side output LO lasts well above 500us. That is creating overcharging on the HB_HS capacitor, which as a result, is causing oscillations and overshoot on the HB node shown in yellow by ch-1. This overshoot and ringing reaches almost 40V, which is well above HB_HS abs max of most modern drivers.
One way to remedy this issue is to increase the HB_HS capacitance value, allowing to increase energy storage capability of the capacitor.
An alternate method is to increase the bootstrap resistor, allowing to reduce peak currents charging the HB_HS network, and therefore increasing the time constant RC to charge the HB_HS capacitor. This time constant occurring during the high side off time or low side on time explains the dependency on duty cycle. This duty cycle being constant, the boot resistor and HB_HS cap should be tuned appropriately to achieve the desired start up time.

## Slide 12
High side boot supply is ready
Driver IC is enabled
PWM input HI&LI are ready
The low side LO is good
EN
HO
VCBOOT
LO
Bias supply
#4 Why is there NO gate driver output?
Notes: The next issue is another half bridge gate driver where the high side HB_HS supply is on and captured by VCboot in blue. The driver is also enabled, as shown by ch-1, the yellow waveform. The PWM input, HI and LI, are both on as well.
The pink curve on the wave form shows the low side output switching normally, but the high side output is flat, stuck to 0V and no switching occurring as shown by the green curve. What could be causing this issue and why?

## Slide 13: #4 Why is there NO gate driver output?
High side boot supply is ready
Driver IC is enabled
PWM input HI&LI are ready
The low side LO is good
There is NO high side output
UVLO delay: 5µs to 100µs depends on the driver
EN
HO
VCBOOT
LO
VDD_ON
50us
Bias supply
Notes: Notice the input LO is enabled well before the HB_HS supply reached the UVLO rising threshold.
This design does not take into account the UVLO delay occurring during powerup, leading to skipped or missing pulses.
We can see the HO pulses switching 50us later after the supply has reached the UVLO rising threshold. This UVLO delay is dependent on the driver and must be accounted for.

## Slide 14: Synchronization LI and HI after bias supplies are both ready
Design guidelines
Turn-on low side to pre-charge boot capacitor
Synchronize HI and LI
Bias supply
Notes: Before the driver is ready to deliver proper output state, there is a power up delay from the UVLO rising edge to output. This delay varies according to the driver. This may be as high as 50us for some drivers.
It is, therefore, recommended to consider proper margin before launching the PWM signal after the drivers bias are ready.
The figures on the right show powerup UVLO delay timing diagram for input and VDD supplies. It is necessary to synchronize the input signals only after the bias supplies are both ready.
This example shows sufficient margin where the PWM signals are launched well after the driver supply has crossed the UVLO threshold.

## Slide 15: #5 What is wrong with the waveform?
Design guidelines:
  Input filter to improve overall system performance
  Decrease loop inductance in PCB layout
Noisy inputs
Normal input
Pin w/ Hi-Z
Notes: The next common issue, we have another bridge topology similar to previous examples.
Ch-1, shows the PWM input INA, CH-2 captures the output while CH-3 in red captures the switch node HS signals and CH-4 the inductor current in DC_DC step down converter application.
Do you see anything wrong with the waveform?
Did you notice the noisy PWM signal coupling to the power stage causing severe overshoot across the system.
During High frequency switching applications, it is common to encounter ground bounce due to high dv/dt and di/dt from the power stage.
This factor combined with poor layout could cause noisy signals on driver’s inputs which will couple throughout the gate drive portion.
Though it is recommended that users avoid shaping the signals to the gate driver in an attempt to slow down (or delay) the signal at the output.
However, a small input RC filter can be used to mitigate the ringing introduced by non-ideal layout or long PCB traces.
Such a filter may use resistor values in the range of 0 Ω to100 Ω and a capacitor values between 10 pF and 100 pF.
When selecting these components, it is important to pay attention to the trade-off between good noise immunity and propagation delay.

## Slide 16
Voltage waveform “VAB” has intermittent failure and glitches
#6 What causes glitches in PSFB at full load?
Pin w/ Hi-Z
Notes: This next issue is a phase shifted full bridge topology where VAB CH-1, captures the voltage across the 2 switch nodes HS and CH-2 capture the phase current.
What could be causing the glitch on the VAB voltage?
I will open up the poll for possible root causes.

## Slide 17: #6 What causes glitches in PSFB at full load?
Output A is being delayed by 1.2µs (which should be <50ns)
INA
OUTA
1.2μs
Pin w/ Hi-Z
Notes: We noticed the glitches on the VAB voltage which may traced back to the one of the bridge driver’s channels increased propagation delays.
In this scenario, CH_A INA to OUTA is being delayed by 1.2us well beyond the typical specification of 50ns. This delay is seen down at the full bridge causing the glitch on the power stage captured here by CH-1.

## Slide 18: Do NOT leave functional pins open
UCC21520
INA
INB
VCCI
VCCI
GND
DISABLE
DT
NC
GNDB
OUTB
VDDB
NC
NC
GNDA
OUTA
VDDA
Design guidelines
  DT pin is left open and noise is coupled into the driver
  For dead time setting, bypass with ≥2.2nF close to DT pin
  DT(in ns) = 10×RDT (in kΩ)
  For overlapping or no DT, tie DT pin to VCCI
Root cause
Pin w/ Hi-Z
Notes: This issue is commonly attributed to leaving functional pins floating which may cause noise coupling into the driver IC. This specific case shows the dead time pin left floating when it should be either tied to an external resistor for dead time setting; OR tied to VCC to allow overlap of the 2 channels.
The functional pins should not be left floating when unused including input pins which should be tied to GND when that channel is not in use.

## Slide 19
SW-Node
VCC
Driver
PWM
P
N
Turn-ON
Turn-OFF
CGD
CGS
CDS
Parasitics in gate driver sub-system
Parasitics
Notes: For parasitics, junction capacitance, pcb trace, wire bond inductance and resistance are all parasitics in the gate drive portion.
Therefore, the turn-on/off will be a little bit more complicated.
For SIC and SI MOSFETs, there is a body diode also considered as parasitics.

## Slide 20
High dV/dt and dI/dt causes D-G capacitor to charge and develop voltage
Voltage may be higher than Vgs(th)
High voltage and IGBT applications
Series gate and gate to source resistor
Driver with Miller clamp
False LO pulse
Parasitics
#7 What Is wrong when HO turns off?
Notes: Back to our typical half-bridge topology from the previous examples, we have low side channel in green, the switch node HS voltage and the high side channel HO.
Assume the VCC and HB_HS bias voltages are all within normal ranges and that PWM signals are also within the recommended operating conditions.
What could be wrong when HO turns off considering parasitic in the gate drive circuit?
I will open the poll while you examine the waveforms and potential root cause?
Notice the false logic on the LO channels which is supposed to saturate to the gate drive voltage when the HO and HS turns off. But instead, LO gets stuck low before eventually reaching the gate drive voltage.
This is typically associate to high dv/dt on the high side channel HO which, IF coupled with high di/dt through the transistor may cause parasitic current at the gate through the Cgd capacitor.
This parasitic current coupled with the gate resistor may develop a voltage at gate which could turn-on the low-side gate if this voltage exceeds the Vgs threshold of the power transistor.
TO address this issue, it is recommended to use a gate to source resistor which will allow the gate to be pulled low while also provide a path for the parasitic Cgd current to GND away from the driver IC output.
A driver with Miller clamp may also address this issue by providing a low impedance to the parasitic currents.

## Slide 21
SW
VGS
15V/div
QRR
IF
VF
Diode reverse recovery
VDS
100V/div
VTH
VGS
VDS
ID
t0
t1
t2a
t2b
t4
t3
ID_pk
Turn-on w/ QRR
Parasitic diode
H-bridge gate driver
IL
QRR
Increase turn-on loss
Higher di/dt, EMI
Device overshoot
Gate drive oscillation (over/under shoot)
#8 Why is the gate drive waveform oscillating?
Parasitics
Notes: IN this scenario, we have the gate to source voltage oscillating shortly after the initial pullup. Consider this case as another half bridge topology.
Why is the gate voltage oscillating? What could be causing the this oscillation?
Please take a moment to brainstorm possible root cause?
Did you guess the power transistor body diode reverse recover losses? If so, yes that is correct. Under hards-witching application, diode reverse recovery will occur. The critical waveform is shown in the top middle.
This reverse recovery current will be reflected to the top switch and generates more turn-on losses.
With two experiment results for body diode of MOSFET and anti-paralleled diode of IGBT, you could see tremendous amount of inrush current, which is caused by reverse recovery.
The driver IC will typically overshoot under such conditions and likely cause EMI issues in the system.
For Si-mosfet, the over-shoot could be over 5 times that of the nominal switching current while IGBTs have relatively smaller overshoot. The main reason is the body diode is a parasitic diode, not optimized, while the body diode in IGBT could be super fast or soft recovery diodes.

## Slide 22
SW
VGS
15V/div
VDS
100V/div
Parasitic diode
H-bridge gate driver
IL
Slow down body diode reverse recovery
FET with robust and low QRR body diode
Soft switching - ZVS
Parasitics
#8 Why is the gate drive waveform oscillating?
Notes: The Reverse recovery property of the body diode of the switching FET is crucial as it can increase losses causing current/voltage overshoot and increase di/dt.
It can also causes gate oscillation as shown
Large di/dt coupled with common source inductance will slow down the switching transitions.
To remedy this issue, it is typically recommended to increase the turn-on resistance and adding an anti parallel diode to separate the turn off time at the gate in an effort to limit the dv.dt at the gate and consequently limiting the di/dt through the power stage.
Another way to remedy this issue is by using ferrite beads with similar impedance that of the gate resistance at the frequency of interest.
Latest topologies will also use soft switching or ZVS to avoid the body diode parasitic losses.

## Slide 23
Gate driver outputs carry high currents and therefore minimize the output loop
If totem pole buffer is used, then place it as close to the power MOSFET as possible
Gate driver output ground and power MOSFET source need to be as short as possible
Minimize high current gate drive loops

## Slide 24: Examples
Bypass capacitor needs to be as close to gate driver IC as possible
VCC, VDD, input filter, DT, EN, DIS
Value and package of the capacitor do matter
GOOD
BAD

## Slide 25
Case 1: output is shorter than input
HO 80ns glitches at HI=high
Double pulse on HI
LI pulled down w/ 4.7kΩ
Missing pulse
HI (5V/div), BW=1GHz
HO (10V/div), BW=200MHz
HS(VDS-Low)
(50V/div)
BW=1GHz
IL (5A/div)
(BW=120MHz)
#9 What is wrong with my HO output?
dv/dt

## Slide 26
Case 2: output is longer than input
HO stretched for 4µs more
Double pulse on HI
LI pulled down w/ 4.7kΩ
HI (5V/div), BW=1GHz
HO (10V/div), BW=250MHz
HS(VDS-Low)
(50V/div)
BW=1GHz
IL (5A/div)
(BW=120MHz)
???
2us/div
dv/dt
#9 What is wrong with my HO output?

## Slide 27
Case 3: output on and off intermittent while HI is ON
HO turns off intermittent
Double pulse on HI
LI pulled down w/ 4.7kΩ
HI (5V/div), BW=250MHz
HS (40V/div), BW=500MHz
HO
(50V/div)
BW=1GHz
IL (5A/div)
(BW=120MHz)
dv/dt
#9 What is wrong with my output?

## Slide 28
INA
SW
(500MHz)
OUTA
IL
Zoom IN
CMTI=285V/ns
Slow down reverse recovery
FET w/ low QRR B-diode
Soft switching - ZVS
The switch node CMTI is >200V/ns
dv/dt

## Slide 29
GND
Minimize or avoid overlapping switch node plane and ground plane
Could create issues when switching frequencies are high
As HS slew rates are high, overlap of ground plane and switch node plane might inject noise in other circuits on the board
Layout: ground plane and switch node (SW)
dv/dt

## Slide 30
HO/LO might cross conduct
  Shoot-through current
  Excessive power dissipation
  False overcurrent tripping
Account for propagation delay and delay matching variation across temperature/voltage
Account for drive strength variation across temperature/bias voltage
May be
#10 Would this waveform create any system problems?
Variance

## Slide 31
Various issues encountered while designing switch-mode power supplies were discussed from the gate driver IC point of view and their resolutions were clearly identified
Proper bypassing of the gate driver IC (as with many other ICs) is extremely critical to its performance
When gate driver IC is used in half-bridge configuration, switch node slew rate plays an important role in the performance of the gate driver IC
PCB layout plays important role in satisfactory performance of the gate driver IC and thus the whole system
Summary

## Slide 32
©2021 Texas Instruments Incorporated. All rights reserved.
SLYP754