## Slide 1: Connect the hardware
Notes: For this experiment we will be using channel 2 on the precision labs hardware. First, set the jumpers as shown here. Connect the PSI to the PLABS board using the SMA cable, and connect the PHI to the PLABS channel 2 connector. Finally, connect the USB cables to the computer. Throughout this experiment we will test different amplifiers. Always be careful to install this amplifier right side up with the label at the bottom of the coupon card. For now you can leave the amplifier socket empty. Pause and connect the hardware.

## Slide 2: Record results as we progress through Experiment
Device |  |  |  |  | Simulated Settling Error ½LSB=38uV | Example Measurements |  | Your Measurements | 
 | Device | Samp.Rate | Voffset (V) | Vin (V) | Verror (V) | SNR (dB) | THD (dB) | SNR (dB) | THD (dB)
 | ADS8860 Data Sheet |  |  |  |  | 93 | -108 |  | 
1 | OPA320 Good filter1 | 1M | 2.5 | 4.9 | 28uV | 93.3 | -108.8 |  | 
2 | OPA320 Bad filter | 1M | 2.5 | 4.9 | -41mV | 82.5 | -73.4 |  | 
3 | OPA333 Low Bandwidth | 1M | 2.5 | 4.9 | -91mV | 54.1 | -55.9 |  | 
4 | OPA316 Crossover | 1M | 1.8 | 3.6 | 36.7mV | 86.1 | -85.0 |  | 
5 | OPA316 Crossover | 500k | 1.8 | 3.6 | 47uV | 90.3 | -102.4 |  | 
Notes: Throughout the experiment we will use different devices and apply different input signal amplitudes at different sampling rates. Also, we will simulate and measure the performance of the different circuits. Print out this table and use it to record your measured results as you step through the experiments.