## Slide 1: Selecting and Verifying the Driver Amplifier TIPL 4402 TI Precision Labs – ADCs
Created by Tim Green, Art Kay
Presented by Peggy Liska
Notes: Hello, and welcome to the TI Precision Lab covering component selection for SAR ADCs. In this video we will learn how to use Texas Instruments parametric search tools to find an amplifier that will meet your application requirements. We will also learn how to verify that the SPICE model is accurate and sufficient for SAR drive simulations.

## Slide 2
Agenda
SAR Operation Overview
Select the data converter
Use the Calculator to find amplifier and RC filter
Find the Op Amp
Verify the Op Amp Model
Building the SAR Model
Refine the Rfilt and Cfilt values
Final simulations
Measured Results
SAR Drive Calculator Algorithm
Notes: This video covers steps 4 and 5 of the process for selecting the external components for a SAR ADC. Let’s start by choosing the right op-amp.

## Slide 3: Find the Op Amp
Channel Count = 1
Supply Voltage = 5V
Gain Bandwidth = 17.8MHz
22 devices left!
Select
Operational Amplifiers (Op Amps)
1464 different choices!
Select Amplifiers
Select Products
Notes: There are over a thousand different amplifiers to choose from, so how do we find the right one. TI’s parametric search engine is a good way to narrow down the choices. To get to this tool, click on the amplifiers product are ti.com. In the amplifiers section click on “operational amplifiers (Op Amps)”. From here, select the “products” tab and use the quick search feature. In this case we want a single channel amplifier, with a 5V supply. Based on the results from the calculator, we need at least 17.8MHz of bandwidth. After entering this information the number of choices is narrowed down to 22 devices.

## Slide 4: Set filters to find the best device
OPA320
Best offset
Use the filters to narrow options
Notes: At this point we can continue to select filters to narrow our options. First we can put an upper limit of 50MHz on the bandwidth. We do this because bandwidth beyond 50MHz is probably overkill for this design. Next, let’s choose a package style. In this case we use SOT-23. DC performance is also important, so we limit the offset to be less than 0.5mV. Finally, we limit the “rating” to be “catalog” devices only. At this point the number of choices is limited to three devices. We select the OPA320 for our design as it has the best offset. Note, that in some cases you may find that no devices meet your criteria. In this case you will have to step back through the filtering process and make some compromises in your design requirements.

## Slide 5: Get the latest model from the web
2. Select the “reference design”. This will be a fully wired example schematic.
3. Press open and TINA SPICE will directly open the schematic.
1. The TINA model is located under tools and software.
Notes: Once you have selected your amplifier you need to get a TINA SPICE model as the ADC drive optimization and verification is done in SPICE. The best way to find the model is to go to the tools and software tab on the ti.com landing page for that product. In some case this model is included with the TINA SPICE software package but it is better to get the model from ti.com as this assure that you get the most up to date model. Also, it is recommend that you download and open the “reference design” as this is a pre-wired test circuit that you can used as the basis for your design.

## Slide 6
Agenda
SAR Operation Overview
Select the data converter
Use the Calculator to find amplifier and RC filter
Find the Op Amp
Verify the Op Amp Model
Building the SAR Model
Refine the Rfilt and Cfilt values
Final simulations
Measured Results
SAR Drive Calculator Algorithm
Notes: Let’s now move on and verify the op-amp simulation model.

## Slide 7: Op Amp Model: Open Loop Gain
Notes: It is very important to verify the accuracy of the model you use for SAR drive simulations. For this kind of application, bandwidth, open loop gain, and open loop output impedance are important to achieve accurate results. Most modern models are sophisticated and cover these and many other parameters. However, it’s easy to check the models and it’s better to be confidant in its operation. This slide shows how you would test the model for open loop gain. First, for this test the amplifier needs to be in the linear operating range. So in this case the input signal is set to 2.5V to make sure that the output is at mid scale and not driving into a rail. The feedback network contains a large 1T Henry inductor to open the loop for AC signals and short the loop for dc signals. This allows for a good DC operating point but keeps the loop open so that we can do open loop analysis. The 1T Farad capacitor disconnects the AC signal for the DC operating point and connects the source for any AC frequencies of interest. In the center we show the TINA spice simulation results, and at the right we show the data sheet specification for open loop gain. To compare two plots look at a few points on the magnitude and phase plot. Some key points to consider are the dc gain, and the unity gain bandwidth on the magnitude plot. In the phase plot check the phase at the unity gain bandwidth frequency. Note that sometimes the phase plot will be off by a 180⁰ as the phase depends on how the circuit is measured. In this example you see good agreement between the simulated results and the data sheet curve.

## Slide 8: Op Amp Model: Open Loop Output Impedance
Notes: Another important curve is the open loop output impedance. This curve is ideally flat and low for fastest ADC settling. The circuit used for this test is similar to the open loop gain test, as the feedback loop is broken for AC but is shorted for DC operation. The output here is connected to an AC current generator, and a voltage measurement probe is included. Also notice that the input is biased so that the output will be in a linear voltage range. Again, for any simulation it is important to verify the DC operation before the AC simulation. This helps avoid problems caused by incorrect wiring. Once the circuit is connected and it’s DC operation was confirmed you can run the “AC Analysis>AC Transfer Characteristic”. For this simulation the output voltage is equal to the open loop output impedance, that is Zo (dB) = Vout (dB). Make sure that you change the vertical axis to logarithmic and scale to match the data sheet curve. In this case, you can see that the simulation result closely matches the data sheet specification so this model has properly modeled open loop output impedance.

## Slide 9: Op Amp Model: Closed loop output impedance
Notes: Some amplifier data sheets will provide an open loop output impedance (Zo) specification, and others will provide a closed loop (Zout) curve. The two curves are directly related so it is sufficient to verify either curve. So in cases where the data sheet provides a closed loop output impedance curve, you can simulate this test circuit. One key tip to decide if the impedance curve is open loop out impedance (Zo) or closed loop output impedance (Zout) is to see if the curve specifies a gain for the test condition. In our example we see three curves and each specifies a gin (G-=1, G=10, G=100) indicating that these are closed loop output impedance curves (Zout). Since this is closed loop impedance the feedback network is set according to the required gain. This example shows a gain of 1, but other gains may be needed depending on the data sheet graph. The output is connected to a current generator and a voltage measurement probe. Closed loop output impedance is equal to the output voltage in this simulation, that is Zout (dB) = Vout(dB). By changing the Y-axis to Logarithmic we get Zout in ohms (Zout(ohms) = Vout(Logarithmic)). Notice that the simulation results closely match the data sheet curve for unity gain.

## Slide 10
Agenda – next video…
SAR Operation Overview
Select the data converter
Use the Calculator to find amplifier and RC filter
Find the Op Amp
Verify the Op Amp Model
Building the SAR Model
Refine the Rfilt and Cfilt values
Final simulations
Measured Results
SAR Drive Calculator Algorithm
Notes: The next video will walk through step 6 of the process.

## Slide 11: Thanks for your time! Please try the quiz.
Notes: That concludes this video – thank you for watching! Please try the quiz to check your understanding of this video’s content.